Dennis Murphy Dayton RS/Seas WMT

As mentioned in another thread Dennis has been working on a WMT using the RS225, RS150, and the Seas 27TBFC/G. After listening to it for a few days he is very happy with the xover so I am making it available now. This speaker uses a smaller cabinet than that of the WWMT and can be used as a stand alone speaker or as a rear channel surround.

It will be left to the end user to decide wether they want a ported or sealed enclosure. Per Unibox cabinet size sealed for a single RS225 enclosure is around 28 liters plus the RS150 enclosure. F3 should be about 50 Hz. Ported should be 50-60 liters with either a 3"x8.72" (50) or a 3"x10.83" (60) long port which will have a F3 in the upper 20's.

Attached are the schematics and the measured response of the speaker along with a reverse null measurement.

These drawings are just a reference, feel free to make any changes you would like. As long as the baffle width and speaker locations are not altered you will be fine.

Also I am not a regular Autocad user so this drawing is not to scale and you should check all measurements before you make any cuts...I have been known to make mistakes in the past...