SS18W/8531G-00 in a 10:1 tapered TL 72" long with input of 2.83v/1m and first ~2/3 of the line stuffed with polyester fiber at a density of 0.75 lb/ft3. Line has a constant width of 7.5", a depth of 10" at its beginning and a depth of 1" at the terminus.  System tuning frequency of 34-35 Hz.  Woofer's center located 14.5" from the beginning of the line, and the terminus (exit) located at the end of the line.

Predicted system bass response (red line) with line continuously tapered from end to end (simulating a single-fold line with angled corner reflectors at its U-turn).

Predicted system bass response (red line) but with line having right-angle corners at the U-turn.